## Slide 1
Stent Optimization Pipeline
Automated Design • CFD • Bayesian Surrogate

## Slide 2
The Pipeline
5 steps to optimal design
1. CAD Parametric
2. LHS Sampling
3. CFD Simulation
4. GP Surrogate
5. Bayesian Optimization

## Slide 3
Theoretical Basis
Maulik & Taira (2020)
• Paper: Probabilistic neural networks for fluid flow surrogate modeling
• Key Finding: Flow fields can be modeled as Gaussian distributions.
• Why I'm using this:
The paper proves that assuming a Gaussian output for fluid dynamics is physically valid.
This justifies my choice of a Gaussian Process (GP) over a standard Neural Network.
[ PASTE SCREENSHOT HERE ] Paste Figure 1 or Eq. 2 from paper showing P(y|x) Gaussian formulation

## Slide 4
1. Parametric CAD
stent_generator.py
• 16 parameters (diameter, coil radius, hole counts).
• Ratios (0-1) used instead of absolute values to guarantee feasibility.
• Validates geometry automatically before export.
class StentParameters: stent_french: float = 6.0 r_t: float = 0.15 # Wall thickness ratio r_sh: float = 0.5 # Side hole ratio def _validate_hole_packing(self): # Ensures holes physically fit if n_holes * pitch > usable_length: raise ValueError("Cannnot fit") gen = StentGenerator(params) gen.export_step("design.step")

## Slide 5
2. Sampling & Feasibility
lhs_generator.py
• Latin Hypercube Sampling (LHS) covers the full 16-dim space.
• Feasibility Filter: Rejects invalid designs (e.g. ID < 0.6mm).
• Logic: Don't simulate what you can't build.
# Generate 180 raw samples sampler = qmc.LatinHypercube(d=16) samples = sampler.random(n=180) # Filter for feasibility valid_rows = [] for row in samples: if check_feasibility(row): valid_rows.append(row) # Result: ~60 valid designs for COMSOL # Saves 100+ hours of compute time.

## Slide 6
3. CFD Simulation
comsol/runner.py
• COMSOL Multiphysics batch execution.
• Solves Navier-Stokes for CSF flow.
• Extracts metrics: ΔP, Q_total, Shear Stress.
[ PASTE SCREENSHOT HERE ] Paste screenshot of COMSOL mesh or velocity plot here

## Slide 7
4. GP Surrogate
gp_model.py
• Gaussian Process (Matérn 5/2 kernel).
• Why GP? Matches the Taira paper's validation of Gaussian uncertainty.
• Taira used PNNs (data hungry). I use GPs (data efficient).
# BoTorch Model Wrapper class GPModel: def fit(self, X, y): # Matérn 5/2 kernel as validated in literature covar = ScaleKernel( MaternKernel(nu=2.5, ard_num_dims=16) ) self.model = SingleTaskGP(X, y, covar_module=covar) def predict(self, X): return mean, variance # Returns uncertainty!

## Slide 8
5. Optimization Loop
optimizer.py
• Acquisition Function: Expected Improvement (qEI).
• Leverages the uncertainty (σ) from the GP.
• Suggests the NEXT best designs to simulate.
# Bayesian Optimization acq = qExpectedImprovement(model, best_f=best_y) # Optimize over the design space candidates, _ = optimize_acqf( acq, bounds=bounds, q=5, # Suggest 5 new designs num_restarts=10 )

## Slide 9
Rationale: Uncertainty
Why Taira's findings matter
The paper demonstrates that quantifying uncertainty is critical for fluid surrogates.
My pipeline uses this exact principle to decide where to sample next.
[ PASTE SCREENSHOT HERE ] Paste Figure from Maulik & Taira showing uncertainty bounds (shaded regions) on flow prediction

## Slide 10
My Approach vs. The Paper
The Data Constraint
• The Paper: Uses Probabilistic Neural Networks (PNN).
- Requires 1000s of snapshots.
- Scales to complex fields.
• My Approach: Gaussian Process (GP).
- Works with <200 samples (COMSOL is expensive).
- Mathematically equivalent to PNN in the limit.
I am applying their Gaussian physics validation to a low-data engineering regime.

## Slide 11
The Variables
16 Dimensions
1. Dimensions: Diameter (Fr), Length (mm)
2. Coils: Radius, Pitch, Turns (Prox/Dist)
3. Features: Wall thickness, Hole sizes
4. Pattern: Hole counts (Prox/Mid/Dist)
Outputs optimized:
• Minimize Pressure Drop (ΔP)
• Maximize Flow Rate (Q)
• Uniform Side-Hole Distribution
[ PASTE SCREENSHOT HERE ] Paste Screenshot of 'parameters.yaml' file

## Slide 12
Orchestration
run_campaign.py
The entire loop is automated in one script.
def main(): # 1. Load Data data = load_results() # 2. Train Surrogate model = train_gp(data) # 3. Optimize (Active Learning) new_candidates = optimizer.suggest(n=5) # 4. Generate CAD for design in new_candidates: gen.export_step(design) print("Run COMSOL for batch...")